Cole Thorpe
Lab Report 2
PHYS 2215
Matthew Pellegrini
Introduction
In this lab we explored the properties of Hooke’s Law, and the interaction of springs. Keep in mind, the circumstances where I conducted this lab was on short time, so my results may be fairly off from usual. We were meant to build springs using 2 different materials, and set them up on an apparatus to test the distance stretched from rest. The primary equation we explored this lab was Hooke’s Law,
F_{spring}=-kx
The different parts of this equation are defined as follows. The left side of the equation, F is the force of the spring, consisting of mass times gravity. The right side of the equation is marked as negative, to signify that the spring is a restoring force. The k represents the spring constant in an individual spring, while x is the distance stretched.
This experiment, although requiring the use of 2 different spring materials, primarily only used one of our choosing. With the first spring we would create three of, then destroying all of them by adding on too much mass to hang, by increasing the number of washers on the hanging end of the spring, as we recorded the stretch.
Procedure
This lab we were provided with the following materials; 2 different wires, 0.7 mm galvanized steel, 1.0 mm copper, various washers, a ruler, a meter stick, bars, and a support rod apparatus with clamps. Using the wire material, we were to wrap it around the bar, creating our own makeshift spring, allowing for the destruction of the spring with minimal consequences. We explored the following topics; Hooke’s Law Limit, the spring constant k, springs of different winding, and springs of different material.
I started the lab (I had no partner) with choosing the primary material of spring and winding gradually adding more washers until the spring was permanently altered, and could not return to a normal state. I chose the 0.7 mm galvanized copper wire as my spring material with 8 windings around the rod. We also recorded the diameter, which from the rod we had was about 2.2 cm. After creating and recording my spring, I discovered that my current setup would result in a destroyed spring after about 10 washers. I was then instructed to make an identical spring.
For my second spring I was only to use 6 washers, slowly adding on each washer and recording the spring’s extension from rest. As we recorded the extension we were to algebraically manipulate the Hooke’s Law formula to solve for k, since we discovered the values of F and x. using our values of k we were to plot out a graph and see if the slope of our graph closely match up with k, which it did with a 13% error. After we determined the spring constant, we continued adding on washers and recording as k got more distorted while we hit Hooke’s Law Limit. We were then instructed to make another spring of the same material
This third spring, although made of the same galvanized copper, was created with half the amount of windings. With the 4 windings I predicted the spring constant value would be about double from the 8 winding counterpart, then I carried out 4 trials to prove this. This may be from error but the spring constant was almost triple more from the previous springs, but took 5 washers to go beyond Hooke’s Law Limit. We were then to create a graph and test our theory which stood. After destroying this spring we switched out material for one more spring.
This final spring, consisted as the usual 2.2 cm diameter and 8 windings, but the material was switched out for steel, rather than the previously used copper. We were to then do as before, adding up to 4 washers onto the wire, recording the extension and calculating the spring constant, and then adding more until the spring was destroyed. This spring was significantly weaker taking 6 washers to reach Hooke’s Law Limit. We were to then explore the differences between the two springs and how the material affects it.
Results
The following tables are the results I’ve gathered from this experiment. I recorded the distance stretched (Extension on table) as the distance change from the bottom of the spring. In hindsight I could of measured the whole spring for more accurate results.
Copper Spring 2 (Determining k)
Trial	Number of Washers	Extension (cm)	k
1	1	0.2	0.75
2	2	0.5	0.6
3	3	1	0.45
4	4	1.2	0.5
5	5	1.5	0.5
6	6	1.5	0.6
		Average k:	0.567
		Uncertainty	0.108
		Uncertainty of the Mean	0.0441

Copper Spring 2 (Destruction)
Trial	Number of Washers	Extension	K
7	7	4	0.262
8	8	4.2	0.25
9	9	5.5	0.191
10	10	7	0.15

Copper Spring 3 (Half Windings)
Trial	Number of Washers	Extension	k
1	1	0.1	1.5
2	2	0.2	1.5
3	3	0.4	1.25
4	4	0.5	1.2
		Average K	1.33
		Uncertainty	0.197
		Uncertainty of the Mean	0.0986

Steel Spring 4 (Alternate Material)
Trial	Number of Washers	Extension	k
1	1	0.5	0.3
2	2	1.5	0.2
3	3	2.5	0.8
4	4	3	0.2
		Average K	0.22
		Uncertainty	0.04195
		Uncertainty of the Mean	0.0209